# Documentation: Quadcopter Waypoint Tracking

## 1. Core Concepts & Physics
### The "Guidance" Approach
This simulation uses a Kinematic Guidance Model. Unlike a "High Fidelity" simulation that calculates the aerodynamics of every propeller blade, this model assumes that if you command a specific tilt angle, the drone achieves it instantly (or with a slight delay).
- Input: Roll, Pitch, Yaw Rate, Thrust.
- Output: Position (X, Y, Z), Velocity, Orientation.
### The Coordinate System (NED)
We use the North-East-Down (NED) frame, which is standard in aviation.
- X Axis (+): North (Forward)
- Y Axis (+): East (Right)
- Z Axis (+): Down (Towards the ground)
- Crucial Note: To fly UP, you must command a Negative Z position (e.g., -5 meters).
## 2. Toolboxes & Block Reference
Block Name	Source	Function & Usage
Guidance Model	UAV Toolbox	The "Plant". It simulates the physics. / Key Setting: Ensure "Control Bus Name" matches your workspace definition to avoid data mismatch errors.
Waypoint Follower	UAV Toolbox	The "Navigator". Takes a list of points and outputs a "Lookahead Point" on the path. / Key Param: LookaheadDistance (smaller = tighter turns, larger = smoother flight).
Bus Creator	Simulink	The "Packager". Bundles 4 individual wires (Roll, Pitch, Yaw, Thrust) into a single Bus object. / Rule: Inputs must be in exact order: Roll $\to$ Pitch $\to$ YawRate $\to$ Thrust.
Signal Conversion	Simulink	The "Translator". Converts a visual bundle (Virtual Bus) into a memory structure (Nonvirtual Bus). / Usage: Essential for fixing "Input bus type mismatch" errors.
MATLAB Function	User Defined	The "Brain". Contains the custom code explained in Section 3 below.

## 3. Deep Dive: Control Logic (Code Explanation)
This logic lives inside the DroneController MATLAB Function block. It uses a PID (Proportional-Integral-Derivative) approach to convert position errors into motor commands.
### The Code Snippet
%Matlab
function control = DroneController(targetPos, targetYaw, currentPos, currentVel, currentYaw)
    % 1. CONFIGURATION
    mass = 2.83; % Mass in kg (Must match the Guidance Model mass)
    g = 9.81; % Gravity acceleration (m/s^2)

    % 2. PID GAINS (The "Tuning Knobs")
    Kp_xy = 1.5; % Proportional Gain for Horizontal movement
    Kd_xy = 1.2; % Derivative Gain (Damping) to prevent overshooting
    Kp_z = 4.0; % Altitude Proportional Gain (Needs to be strong to fight gravity)
    Kd_z = 2.5; % Altitude Damping
    Kp_yaw = 1.5; % Yaw Gain

    % 3. CALCULATE POSITION ERROR
    posErr = targetPos - currentPos;

    % 4. CALCULATE DESIRED VELOCITY (P-Control)
    velDes = posErr * Kp_xy;

    % Safety: Limit Max Speed to 5 m/s
    maxSpeed = 5;
    if norm(velDes) > maxSpeed
        velDes = (velDes / norm(velDes)) * maxSpeed;
    end

    % 5. CALCULATE DESIRED ACCELERATION (PD-Control)
    accDes = (velDes - currentVel) * Kd_xy;

    % Altitude is treated separately (Vertical PD Control)
    accDes(3) = (posErr(3) * Kp_z) - (currentVel(3) * Kd_z);

    % 6. COORDINATE TRANSFORMATION (World Frame -> Body Frame)
    % The calculated acceleration is in the "World" (North/East).
    % But the drone can only tilt relative to itself (Forward/Right).
    % We must rotate the vector based on the drone's current Yaw (Heading).
    psi = currentYaw;
    rotation = [cos(psi) sin(psi); -sin(psi) cos(psi)];
    bodyAcc = rotation * [accDes(1); accDes(2)];

    % 7. CONVERT ACCELERATION TO TILT ANGLES
    % Tilting Forward (Pitch) creates forward acceleration.
    % Tilting Right (Roll) creates rightward acceleration.
    % We divide by 'g' to convert m/s^2 into Radians (small angle approximation).
    cmdPitch = -bodyAcc(1) / g;
    cmdRoll = bodyAcc(2) / g;

    % Safety: Clamp Tilt to ~30 degrees (0.5 radians)
    maxTilt = 0.5;
    cmdPitch = max(min(cmdPitch, maxTilt), -maxTilt);
    cmdRoll = max(min(cmdRoll, maxTilt), -maxTilt);

    % 8. CALCULATE THRUST (Physics Formula)
    % In NED frame, 'g' is positive (down). 'accDes(3)' is negative (up).
    % F_net = Mass * Acceleration
    % Thrust must overcome Gravity AND provide the desired acceleration.
    cmdThrust = mass * (g - accDes(3));

    % 9. YAW CONTROL
    % Simple P-Control to point the nose at the target heading
    yawErr = targetYaw - currentYaw;

    % Normalize angle to keep it between -180 and +180 degrees (in radians)
    while yawErr > pi, yawErr = yawErr - 2*pi; end
    while yawErr < -pi, yawErr = yawErr + 2*pi; end
    cmdYawRate = yawErr * Kp_yaw;

    % 10. OUTPUT
    control = [cmdRoll, cmdPitch, cmdYawRate, cmdThrust];
end
### Key Logic Explained
- Lines 24-27 (Velocity Limit): Without this, if the target is far away, the drone would try to fly at infinite speed, tilt 90 degrees, and crash. We clamp it to 5 m/s.
- Lines 41-42 (Rotation Matrix): This is critical. If the drone is facing East, and you tell it to "Go North", it needs to fly "Left". This matrix math handles that "World" vs "Body" translation.
- Line 62 (Thrust): Why g - accDes(3)? In NED, Gravity is $+9.81$. To fly UP, accDes(3) is negative (e.g., $-2$).
  - $9.81 - (-2) = 11.81$.
  - This means we need MORE thrust than just hovering (9.81) to push the drone up.
## 4. Deep Dive: The Setup Script
The setup_drone_complete.m script performs "Magic" to prevent Simulink errors. Here is how the Bus Generation logic works.
### The Code Snippet
Matlab
% 1. FIND THE BLOCK
modelName = 'Drone_UAVScenario';
blk = find_system(modelName, 'BlockType', 'SubSystem', 'Name', 'Guidance Model');

% 2. RESET DEFINITIONS (The "Magic" Command)
% This command forces the Guidance Model to re-write the Bus definitions in the workspace.
uav.sluav.internal.guidancemodel.mask.createUAVBuses(blk{1});

% 3. CREATE MATCHING DATA STRUCTURES
% Instead of typing "envData.Gravity = ...", we ask MATLAB to build the structure
% based on the definition it just created. This prevents typos.
envData = Simulink.Bus.createMATLABStruct('MultirotorGuidanceEnvironmentBus');

% 4. SCALAR VS VECTOR CHECK
% Some versions of the block want Gravity as '9.81' (Scalar), others want '[0 0 9.81]' (Vector).
% This logic checks the definition and adapts automatically.
gravElem = MultirotorGuidanceEnvironmentBus.Elements(strcmp({MultirotorGuidanceEnvironmentBus.Elements.Name}, 'Gravity'));

if isequal(gravElem.Dimensions, 1)
    envData.Gravity = 9.81; % Scalar mode
else
    envData.Gravity = [0 0 9.81]; % Vector mode
end
### Why is this needed?
Simulink is extremely strict about types. If a block expects a specific C-struct (Bus) and you provide a loose variable, it crashes. This script asks the block exactly what it wants and builds the data to match, guaranteeing 100% compatibility.

## 5. How to Import Waypoints from Excel
To make the path customizable without coding, we use Excel.
### A. Excel File Format
Create a file named flight_path.xlsx. Do not use headers.
- Column A: X Coordinate (North)
- Column B: Y Coordinate (East)
- Column C: Z Coordinate (Altitude - Must be Negative)
A	B	C
0	0	-5
20	0	-5
20	10	-8

### B. Code Modification
In setup_drone_complete.m, look for the Waypoints section and use this logic:
Matlab
disp('Reading waypoints from Excel...');
excelFileName = 'flight_path.xlsx';

if isfile(excelFileName)
    % readmatrix reads the Excel sheet into a MATLAB matrix
    raw_data = readmatrix(excelFileName);

    % Validation: Ensure we have at least 3 columns (X,Y,Z)
    if size(raw_data, 2) >= 3
        waypoints = raw_data(:, 1:3);
        disp([' Loaded ' num2str(height(waypoints)) ' waypoints.']);
    else
        error(' Excel file error: Must have 3 columns (X, Y, Z).');
    end
else
    warning(' File not found. Using default square path.');
    waypoints = [0 0 -2; 10 0 -2; 10 10 -2; 0 0 -2];
end